## Slide 1: Unit 1: Scientific Method
This unit will cover some basic skills you will need in chemistry this year
Measurement
Significant Digits
Units
Dimensional Analysis
Scientific Notation
Graphing
When we are done, you will be held responsible for using these skills all year long
whenever it is needed
Write this in your notes

## Slide 2: Measurement
Students will be able to (SWBAT) properly make measurements on both analog and digital devices
Write this in your notes

## Slide 3: What is Measurement?
The assignment of a number to a characteristic of an object or event, which can be compared with other objects or events
Measurement is the cornerstone of experimentation and science
In science, a specific technique is required in order to make a measurement properly

## Slide 4: Number vs Digit
2
4
.
9
0
This is a number
– shows all the digits associated with a particular value
This is a digit
– a number between 0 and 9 with particular place value
Tens Digit =
2
Ones Digit =
4
Tenths Digit =
9
Hundredths Digit =
0
Write this in your notes

## Slide 5: So How Do We Measure?

## Slide 6: Proper Reporting of Measured Data
Report all known digits
  All digit you can actually read off of the measurement device
Report the first estimated digit
  One digit beyond what you can actually read off of the measurement device
Write this in your notes

## Slide 7: Applying the Rules
Digits you can read off of this ruler
The 1 cm digit
The 0.1 cm digit
Digits you can estimate with this ruler
The 0.01 cm digit
These are the known digits
This is the
first estimated digit

## Slide 8: Reporting by the Rules
3 cm is a known digit
0.5 cm is a known digit
0.07 cm is an estimated digit
1) All known digits
2) One estimated digit
Length with this ruler
3.57 cm

## Slide 9: Proper Reporting of Measured Data
Report all known digits
  All digit you can actually read off of the measurement device
Report the first estimated digit
  One digit beyond what you can actually read off of the measurement device
REVIEW

## Slide 10: Check for Understanding 1
Given this ruler as the measuring device, what is the proper way to report the length of this metal rod?
5.23 cm

## Slide 11: Check for Understanding 2
The volume of fluid in a graduated cylinder is read from the bottom of the meniscus (dotted white line)
What is the proper volume to report?
Units are milliliters (mL)
8.62 mL

## Slide 12: Check for Understanding 3
What is the proper way to report the temperature recorded on this Celsius thermometer
39.40 °C

## Slide 13: Impact of Instrument Type
Analog
Have a physical scale
Magnitude is measured either directly or indirectly
Digital
Have an electronic number display
Magnitude is converted into an electronic signal

## Slide 14: Which is analog & which is digital?

## Slide 15: For Analog Instruments

## Slide 16: For Digital Instruments
If the displayed numbers are unchanging, then
all are known digits
there is no first estimated digit

## Slide 17: For Digital Instruments
If the displayed numbers are unchanging, then
all are known digits
there is no first estimated digit
If some displayed numbers are fluctuating, then
the unchanging displayed numbers are known digits
the first fluctuating digit is the first estimated digit

## Slide 18: Key Points
Write this in your notes
Everyone should have the same number of digits
Everyone should have the same known digits
Everyone should have first estimated digits that are similar if not identical
In this way, the Rules of Measurement give us confidence that each digit of a measured number is correct and reproducible
1
2
3
4
7
4
.
0
3

## Slide 19: Measurement Lab
In your lab groups, you are going to make actual measurements in lab
Each group should get one lab sheet and then move through all stations to record their answers
When done, we will review
Show your sheet to me for a completion grade

## Slide 20: Lab Partners
You now need to pick your lab partners for this lab
Be sure to pick your lab partner(s) wisely
All lab work and report writing will be done together
Everyone in your group will get the same grade
You will have to conduct lab work and report writing even if your lab partner(s) is absent
Do your fair share, or next time, you may be alone!

## Slide 21: Measurement Lab
ANY QUESTIONS?
Get in your lab groups and get on some goggles

## Slide 22: Station 1
Using a ruler, measure the length of the straight vertical pipe on the lab faucet on the front bench.

## Slide 23: Station 2
Using dial calipers, measure the diameter of the gas turret base on the front bench.
If you do not know how to use this device, please review the
Dial Caliper Instructions

## Slide 24: Station 3
Using the electronic balance, measure the mass of a lab spatula

## Slide 25: Station 4
Using the Ohaus electronic balance, determine the mass of a single red pony bead.
Because one bead’s mass is so small, measure the mass of 17 and divide to get weight of one bead.

## Slide 26: Station 5
Read the volume of colored water in the graduated cylinder

## Slide 27: Station 6
Determine the mass of a single ball magnet
Measure 17 ball magnets in a graduated cylinder by water displacement

## Slide 28: Station 7
Using the thermometer on top of the oven, measure the internal temperature of the oven

## Slide 29: Station 8
Measure the volume copper foil using water displacement in a 200 mL flask

## Slide 30: Station 9
Measure the amount of colored water in the large Erlenmeyer flask

## Slide 31: Station 10
Measure the amount of colored water in the burette
PLEASE BE CAREFUL, ESPECIALLY WITH THE BURETTE TIP

## Slide 32
Chemistry
Measurement Lab
Partner 1
Period
Date
Partner 2
Partner 3
Station 1 |  | Station 6 | 
 | Final Answer |  | Final Answer
Station 2 |  | Station 7 | 
 | Final Answer |  | Final Answer
Station 3 |  | Station 8 | 
 | Final Answer |  | Final Answer
Station 4 |  | Station 9 | 
 | Final Answer |  | Final Answer
Station 5 |  | Station 10 | 
 | Final Answer |  | Final Answer

## Slide 33
Chemistry
Measurement Lab
Partner 1
Period
Date
Partner 2
Partner 3
Station 1 |  | Station 6 | 
 | Final Answer |  | Final Answer
Station 2 |  | Station 7 | 
 | Final Answer |  | Final Answer
Station 3 |  | Station 8 | 
 | Final Answer |  | Final Answer
Station 4 |  | Station 9 | 
 | Final Answer |  | Final Answer
Station 5 |  | Station 10 | 
 | Final Answer |  | Final Answer
ANSWERS